## Slide 1: Ralph Zander & Christian Dratwa, 16.11.2019
Radiation aspects of space weather
in the airline business

## Slide 2: Radiation aspects of space weather in the airline business
What you can expect from this talk
Short introduction of „Vereinigung Cockpit“ and our work
Problems we face today
Who is affected in what way
Possible countermeasures
Your questions, short discussion
Aviation pictures
Intro, Ralph Zander, VC, 1.11.2019

## Slide 3: Radiation aspects of space weather in the airline business
„Vereinigung Cockpit“ – WHO WE ARE AND WHAT WE DO
Vereinigung Cockpit is the german airline pilots association, part of ECA (European Cockpit Association)
Different units, taking care of the interests of pilots; e.g. air traffic services, flight health, radiation
Who is presenting this talk
Intro, Ralph Zander, VC, 16.11.2019

## Slide 4: Radiation aspects of space weather in the airline business
ProblemS we face today
Problem, Ralph Zander, VC, 16.11.2019
Is occupational radiation exposure an issue at all?
The Federal Office for Radiation Protection (BfS) figures for Germany in 2017
  Monitored occupationally exposed persons: 447,787 thereof air crew: 44,763 (10%)
  Collective dose: 117 Sv thereof air crew collective dose: 93 Sv (79,6%)
The vast majority of exposed workers receives only a minor portion of the dose. Among radiation protection experts, aviation generally serves as the bad example in terms of exposure.
Chart: Occupationally Exposed Persons
| All Others | Crew
Occupationally Exposed Persons | 90 | 10
Chart: Collective Dose
| All Others | Crew
Occupationally Exposed Persons | 20.4 | 79.6
Chart: Occupationally Exposed Persons
| All Others | Crew
Occupationally Exposed Persons | 90 | 10
Chart: Collective Dose
| All Others | Crew
Occupationally Exposed Persons | 20.4 | 79.6
Reasons
The Federal Office for Radiation Protection (BfS), figures for Germany in 2017
Lack of knowledge (Crews, Operators, Legislators)
Increasing pressure by economy
  Increasing flight hours for crews (optimized rostering)
  Flightroutes optimized by economical factors
Lack of countermeasures against imminent dangers (in flight)
  No measurement equipemnt on board
  No space weather reports to crews
1)
1)

## Slide 5: Radiation aspects of space weather in the airline business
Who is affected in what way
Who is affected, Ralph Zander, VC, 16.11.2019
Flight Crew
Communication/Navigation: HF com, GPS distortion
Health: UV radiation & ionizing radiation
Denial or overcautious, Lack of knowledge

## Slide 6: Radiation aspects of space weather in the airline business
Who is affected in what way
Who is affected, Ralph Zander, VC, 16.11.2019
Cabin Crew
Health: ionizing radiation
Lack of knowledge
Common perception: We can‘t do anything against radiation

## Slide 7: Radiation aspects of space weather in the airline business
Who is affected in what way
Who is affected, Ralph Zander, VC, 16.11.2019
Passengers
Lack of knowledge
Frequent flyers
Influence on pregnancy (ionizing radiation)?

## Slide 8: Radiation aspects of space weather in the airline business
Who is affected in what way
Who is affected, Ralph Zander, VC, 16.11.2019
Operators, Crew scheduling, Flightplanning
Denial of risks
Lack of training
Economic pressure

## Slide 9: Radiation aspects of space weather in the airline business
Who is affected in what way
Who is affected, Ralph Zander, VC, 16.11.2019
Legislators
Lack of detailed information
Economic interests
Picture By Saeima - 12.Saeimas deputātu svinīgais solījums, CC BY-SA 2.0, https://commons.wikimedia.org/w/index.php?curid=36631259

## Slide 10: Radiation aspects of space weather in the airline business
Possible countermeasures
Countermeasures, Ralph Zander, VC, 16.11.2019
Smart rostering of crews, educate the crew scheduling staff
Adaption of flight routes/altitudes and taking space weather into account during flight planning, educate dispatch staff
Air traffic control needs to be involved in space weather anomaly procedures
Passenger awareness should be raised, they can build economic pressure on airlines
Operators need to be shown the advantages of educated crews and an action plan
Legislators need an up to date legal framework and installment in airlines
Science should provide methods and equipment for calculating, measuring and forecasting

## Slide 11: Let‘s hear your questions!
Thank you for your attention