## Slide 1: Applications and Models for Satellite Anomaly Analysis Janet Green (Space Hazards Applications, LLC) R. Quinn, Y. Shprits, J. Likar, A. Kellerman, P. O’Brien, S. ClaudePierre, A. Boyd, S.Huston, P. Whelan. N. Reker
Background image:: ESA

## Slide 2: The Issue
Space
weather
Image Credit NASA/SDO
On-orbit anomaly
Surface charging
Internal Charging
Single Event Effects
Total Dose Effects
Increased
particle
radiation
Background image:: ESA
Service outage
Mission Loss
Anomaly Attribution
  Guides response
  Predicts future occurrences
  Leads to improved design

## Slide 3: The Concern
New services rely on large constellations:
Satellite internet, Satellite Imaging
Growing industry and increasing reliance on constellations
SIA 2017
Space News 2019

## Slide 4: Ideal Attribution Tool
Intensification of particle radiation due to space weather leads to anomalies.
The ideal tool would have:
Environment (model or data)
Engineering effect
User Interface
1) Global RT data or environment model to give particle flux along any satellite orbit.
2) Method to translate flux to effect, i.e. hazard quotient, SEE upset rate etc.
3) All brought together in an easy to use and access interface with real time/ retrospective info
Calculate anomalies
Gorini 2012
Image Credit NASA

## Slide 5: The Challenge
Surface Charging:
Low to medium energy particles associated with substorms during moderate Kp activity in the dusk magnetospheric regions.
Internal Charging:
Higher energy electrons associated with some storms that peaks around L=4
Single Event Upsets:
Solar Proton Events associated with solar flares and coronal mass ejections
Total Ionizing Dose:
All of the above.
Environment (model or data)
Engineering effect
User Interface
Accurate RT global models do not exist for all particle populations, effects tools are not always coupled to environments, no common user interfaces.

## Slide 6: Current Attribution
Anomaly Investigation/Monitoring
Limited data difficult to compare to full mission
Fluxes need to be translated into the four specific hazards
Fluxes at GEO do not describe full magnetosphere
“Knowing what we know now this process should be automated.”
Some anomalies go undiagnosed because attribution is a research project requiring significant time and expert knowledge

## Slide 7: SHELLS
The project will deliver a data driven global specification of Earth’s high energy electron environment that includes retrospective, real time, and forecast outputs using machine learning techniques.
Specifying High-altitude Electrons Using Low-altitude LEO Systems (SHELLS)
Image Credit NASA
Image Credit NOAA/NASA

## Slide 8: SHELLS
Uses a neural network to learn the mapping from low altitude POES electron flux to near equatorial Van Allen Probes fluxes
With the learned mapping, electron flux can be specified from L=2-6 at equatorial/off equatorial regions using Kp and POES
Will produce a long-term (solar cycle) history of the environment and real-time nowcast/forecast
Could be used for data assimilation input to physics models
Specifying High-altitude Electrons Using Low-altitude LEO Systems (SHELLS)
NN mapping

## Slide 9: SHELLS
Specifying High-altitude Electrons Using Low-altitude LEO Systems (SHELLS)

## Slide 10: About SatCAT
Allows users to respond quickly and confidently with the right action
The Satellite Charging Assessment Tool
Is an online interactive web application that allows users to generate, display, and analyze an accumulated charge history for a user chosen satellite, shielding, and materials
Provides recent mission history and updates in real time
Environment (model or data)
Engineering effect
User Interface
VERB
Bodeau, 2010
Spacehaz.com/satcat2.html

## Slide 11: SatCAT
Anomaly Investigation
Secure user login
Choose satellite from Spacetrak catalogue, shielding thickness, material
Generate a dataset that is stored in a database and updated in real time

## Slide 12: SatCAT
Anomaly Investigation
Add anomaly points to plots
Plot and download data and images

## Slide 13: SatCAT
Anomaly Investigation
Statistical plots

## Slide 14: SPAM
Fit low (POES) and high altitude (HEO) proton fluxes to Weibull functions
Regress POES/HEO parameters in 4 MLT quadrants to create a mapping function from high to low altitudes
Once the mapping function is established SEP fluxes can be mapped throughout the magnetosphere with just POES
POES real time mapping captures more of the dynamic proton access than statistical models.
Intended for Attribution of SEU’s caused by Solar Energetic Particles
Weibull Fit

## Slide 15: Summary
Changes in the satellite industry (use of large constellations) may make anomaly analysis more critical.
Tools are needed that bring together data/models with physics/engineering understanding to simplify anomaly attribution and make the process accessible and feasible for end users.
Additional models and interfaces are needed for comprehensive attribution that addresses 4 types of hazards.
Internal charging:
  SHELLS neural network radiation environment
  SatCAT
SEE:
  SPAM (Solar Particle Access Model)