## Slide 1: The GOES EUVS Model: New Operational Spectral Irradiances from GOES-R
Edward M.B. Thiemann1, Francis G. Eparvier1, Thomas N. Woods1, Andrew R. Jones1, Martin Snow1, Donald L. Woodraska1, Janet Machol2
Planetary Science • Space Physics • Solar Influences • Atmospheric Science • Engineering • Mission Operations & Data Systems
http://lasp.colorado.edu
Laboratory for Atmospheric and Space Physics, University of Colorado, Boulder, USA
NOAA Space Weather Predictions Center, Boulder, USA
Notes: Note: This template has some issues with older versions of PowerPoint. Please ensure you are using the latest version (which is a free upgrade on LASP computers).

## Slide 2: A Need for Calibrated EUV Irradiance
Solar EUV radiation is the primary energy input to the Earth’s upper atmosphere.
  Creates the dayside ionosphere and heats the thermosphere.
EUV irradiance is a key (if not the) major input into physics-based upper atmospheric models for research and space weather forecasting.
It’s highly structured in wavelength and variable in time.
  Integrated ionizing irradiance varied by ~50% over the past solar cycle.
  ~15% variability common during a 27-day solar rotation period.
  ~100% increase during X10 flares, occurring in minutes.
Therefore, time dependent EUV irradiance spectra are needed to estimate the state of the upper atmosphere.
  Direct measurements (Drawbacks: spectrally incomplete, higher latency).
  Models (Drawbacks: higher uncertainty).
Solomon & Qian JGR 2005
EUV Power Deposited In
Earth’s Atmosphere

## Slide 3: EUV Measurements: Past, Present and Future
Since January 2017 and planned through 2035, GOES EXIS will measure 7 lines from 25-141 nm at <10 s cadence and 30 second latency.
  These lines drive the GOES EUVS Model, which has been calibrated against SEE and EVE.
F10.7 Driven Models
The EUVS Model

## Slide 4: EUV Proxy Modeling
The demand for EUV irradiance estimates over a wide range of time led to the development of EUV proxy modeling.
  Hinteregger81
  EUVAC
  FISM
They decompose irradiance into multiple time scales.
Use measurements of emissions that form at similar regions in the Sun’s atmosphere to model unmeasured emissions.

## Slide 5: GOES-R EUV and X-ray Irradiance Sensors
EXIS = EUV and X-ray Irradiance Sensors
The Key Components of EXIS:
EUVS = Extreme Ultraviolet Sensor
XRS = X-Ray Sensor
EXEB = EUVS/XRS Electrical Box
A2:
Solar max/flare
λ = 0.05-0.4nm
Dark
Dark
A1:
Solar min
λ = 0.05-0.4 nm
B1:
Solar min
λ = 0.1-0.8 nm
B2:
Solar max/flare
λ = 0.1-0.8nm
XRS
EUVS

## Slide 6: The GOES EUVS Model for EUV Irradiance
EUVS model uses EXIS measurements with set of regression coefficients at two time-scales to reconstruct EUV irradiance spectra.
  Daily average and 1 second variability around the daily average.
  Multi-linear regression and broad range of formation temperatures represented by EXIS negates the need for solar cycle/rotation decomposition.
NOAA primary low latency model resolution is coarse.
  5 nm bins from 5-115 nm and one 117-127 nm (Ly-α) bin
Additional secondary binning will also be distributed.
  1 nm resolution
  Stan-band binning

## Slide 7: EUVS Model Calibration Methods
The SEE and EVE datasets are used with overlapping simulated. EXIS measurements to find model coefficients using linear regression methods with multiple inputs.
Simulated EXIS measurements are cross-calibrated with EXIS line irradiances.
  Do not use XRS emissions b/c they tend to increase model error
Model uncertainties are combination of how well historical data are reproduced by the model using simulated EXIS measurements and the cross-calibration between EXIS and the overlapping simulated measurements.

## Slide 8: EXIS Measurement Cross-calibration
EUVS A
EUVS B
Cross-Calibration Uncertainty
25.6 nm
28.4 nm
30.4 nm
117.5 nm
121.6nm
133.5 nm
140.5 nm

## Slide 9: Sample EUVS Model Daily Average Results
EVE Based Bins
SEE Based Bins

## Slide 10: EUVS Model Uncertainty: Daily Average Irradiance
Model uncertainty is combination of how well model reproduces measurements and cross-calibration of simulated and actual EXIS measurements.
Model uncertainty at 5 nm resolution is very low, < 3% for most bins.

## Slide 11: EUVS Model Flare Component Results
Flare component found using > M flares from EVE and GOES EUVS-E.
  248 flares 6-35 nm
  60 flares 35-105 nm
Found limb-ward flares increased overall model error at longer wavelengths.
  Model does not explicitly adjust for flare limb darkening
  Model trained with flares <45o from disk-center.
  Model uncertainty increases somewhat for limb-ward flares.
9.5 nm (Fe 18)
19.5 nm (Fe 24)
17.5 nm (Fe 9)
28.5nm (Fe 15)
30.5 nm (He 2)
97.5 nm (Ly-γ, C 3)

## Slide 12: EUVS Model Flare Component Results
Flare component found using > M flares from EVE and GOES EUVS-E.
  248 flares 6-35 nm
  60 flares 35-105 nm
Found limb-ward flares increased overall model error at longer wavelengths.
  Model does not explicitly adjust for flare limb darkening
  Model trained with flares <45o from disk-center.
  Model uncertainty increases somewhat for limb-ward flares.
Marked improvement over FISM-M b/c EUV lines are much better proxy than soft x-rays.
EUVS Model
FISM-M
Thiemann et al. JGR 2017
9.5 nm (Fe 18)
19.5 nm (Fe 24)
17.5 nm (Fe 9)
28.5nm (Fe 15)
30.5 nm (He 2)
97.5 nm (Ly-γ, C 3)

## Slide 13: Summary and Conclusions
A new era has begun with GOES-R as the collection of an extended record of EUV irradiances has begun, with an anticipated research value comparable to the GOES soft x-rays measurements.
The EUVS Model format is at 5 nm bins from 5-115 nm + Ly-α.
  Additional 1 nm and Stan Band binning will also be available.
Daily average spectral irradiance uncertainty is very low < ~3% typ.
Flare irradiance error is much smaller (~50-80%) than FISM models.
  EUV lines much better than soft x-rays for flare EUV irradiance modeling. FISM should incorporate EUV emissions where available.
Provisional GOES EUVS Model data will be made public in early 2019. A paper describing the model to be submitted later this month.

## Slide 14: Questions?

## Slide 15: EUVS Model Calibration Datasets